## Slide 1
01 / 05
HACKARIZONA — TEAM 10
Nuclear
Derating
Forecaster
Forecasting weather-driven nuclear power loss 1 to 14 days ahead so operators can capture energy that would otherwise be left on the table.

## Slide 2
02 / 05
THE PROJECT
What We Built
— Uses historical data to predict how much power a nuclear plant will actually be able to produce over the next 14 days
— Combines weather, river temperature, and streamflow with the plant's own historical performance
— Delivered through a simple web dashboard with a live US map and per-plant detail pages
— Lets operators see trouble coming before it shows up on the grid
— Built on public data only — no proprietary feeds, fully reproducible

## Slide 3
03 / 05
THE PROBLEM
What Is Derating, And Why It Hurts
— Derating is when a plant is forced to run below full power — capacity is there, but it cannot be used
— Driven by hot weather and warm river water — cooling intake limits force operators to throttle down
— Hits hardest during heatwaves, exactly when the grid needs every megawatt the most
— A single summer of derating can cost $50M+ at one plant, $200M+ industry-wide each year
— Today operators react after the dip starts — there is no public forecast of when it is coming
— Result: wasted clean energy, expensive last-minute fossil backup, and avoidable grid strain

## Slide 4
04 / 05
OUR APPROACH
How The Forecaster Solves It
— Outputs a three-tier alert for each day in the forecast window — operational, watch, or alert — alongside the predicted output percentage and an uncertainty band so operators see both the expected value and the range of likely outcomes
— Trained on 20+ years of plant power records, weather, and river data
— One model per forecast horizon (1 through 14 days) — every day on the curve gets its own prediction
— Uses live weather forecasts to project conditions forward, then translates those into expected plant output
— Includes a replay mode proving the model would have called past heat-driven dips in advance
— Architecture is plant-agnostic — adding a new reactor is a single config entry

## Slide 5
05 / 05
THE IMPACT
Who Wins When We Get This Right
ENERGY OPTIMIZATION
— Recover lost megawatts by scheduling maintenance and refueling around predicted dips — capturing even 10% of the U.S. fleet's annual weather-driven derating losses is an estimated ~$20M per year
— Smarter cooling tower usage — operators know when to spin them up and when they will not be needed, saving water and auxiliary power
— Plan backup power in advance — grid operators can line up cheaper replacement generation days ahead instead of paying premium rates for emergency peaker plants once a heatwave hits
— Lower carbon grid response — clean baseload stays online longer
WHO BENEFITS
— Plant operators — fewer surprises, better dispatch decisions
— Grid operators (ISOs / RTOs) — earlier visibility into capacity risk
— Ratepayers — less reliance on costly backup generation during peak demand
— The grid as a whole — a more resilient, lower-emission energy system